## Slide 1
Presented by:
DOU Yuhan
FORCIOLI Quentin
GHAOUI Mohamed Anis
TERRACHER Audrey
Paris-Saclay University
2020 February 03
A2 : Embedded Electronic Systems
Heterogeneous architecture for Big Data algorithms
Final presentation

## Slide 2
TEAM
Software:
    DOU Yuhan
    TERRACHER Audrey
Hardware:
    FORCIOLI QUENTIN
HLS and lead :
    GHAOUI Mohamed Anis
Objective : Complete a full development cycle

## Slide 3
Our approach and algorithms chosen
BMM
Pi Estimator
K-Means
PCA/SVD
Pearson correlation

## Slide 4
Software – PC Implementation

## Slide 5
Software – ARM Implementation
Blocks design
Report

## Slide 6
Software – ARM Implementation
Design on Vivado SDK
1/ Tools Chain : Xilinx ARM v7 GNU Toolchain
Generator : GNU make
2/ Modification of heap and stack sizes :
1 KB (default) → 250 MB

## Slide 7
Software – ARM Implementation

## Slide 8
Software – ARM Implementation
Software optimization
Three main aspects :
1/ branches delays
2/ use of cache
3/ data dependencies
Optimization options for GNU :
- O0 : no optimization
- O1 : optimization on branches
- O2 : optimization at the registers and instruction level
- O3 : optimization at the highest level (eSIMD vectorization , “inline”...)
- Os : optimization on code size

## Slide 9
Software – ARM Implementation
Code size (segmentation “text”) Execution times

## Slide 10
Software – Microblaze Implementation
Blocks design
Report

## Slide 11
Software – Microblaze Implementation
Design on Vivado SDK
1/ Changes in libraries and functions used for timing :
xtime_l.h for ARM Implementation
xtmrctr.h for Microblaze Implementation
2/ Several bugs launching FPGA programming..

## Slide 12
High – Level Synthesis
Reanalyse the algorithms
Directive usage to infer RTL blocks
Implement Axi/Axilite interfaces
Manage and reshape memory
Automated material optimisations

## Slide 13
High – Level Synthesis
AXI/lite Interface directives :
Top-Level function : BUS CONTROL
Inputs
Outputs
Addresses managed by the CPU
While (condition){
do_stuff();
}
For (n iterations){
do_stuff();
}
Control sequence conversion :

## Slide 14
High – Level Synthesis
Initialisation
Perpare data
IP HLS
Send
Receive
Initialisation
Préparation
des
données
Initialisation
de l’algothime
Envoi
Réception
IP HLS 1
Envoi
test
Fin
Fin
Reception
IP HLS 2

## Slide 15
High – Level Synthesis : scheduler
Analyse dependencies
Minimise Initialisation interval
Respect timing and FPGA resources limits
If necessary : reshape the arrays

## Slide 16
High – Level Synthesis : Synthesis
Not always necessary/possible to pipeline all the loops
HLS must respect time constraints
Optimisation can be very time/resource costly

## Slide 17
Architecture exploration
First design used by the SW team
2nd design using BRAM
3rd design with BRAM and HLS IP (still in development)

## Slide 18
Interfacing Zynq to HLS IP
Using ACP port => Cache coherency
Having different clock domains

## Slide 19
Improving clock with timing
Using Timing report to increase HLS clock frequency
Using more performance-oriented placement and synthesis strategies

## Slide 20
Performance
First time @ 100MHZ
Test on MUL64:
  AXI@180MHZ
  HLS@131MHZ
  Acceleration : 320%
IP | HW time (µs) | SW time (µs) | Improved clock | Improve HW times (µs) | Best acceleration
mul64 | 10280 | 26132 | 130MHZ | 7042 | 271%
mul32 | 2412 | 3282 | 125 MHZ | 1810 | 81%
pearson | 32 | 5 | 115 MHZ | 21 | -74%
kmeans | 1297 | 1527 | 120MHZ | 1082 | 41%

## Slide 21
Future improvement
Using interruption instead of polling
A microblaze handle every task involving IP
Multi-microblazes multi-IPs.

## Slide 22
Conclusion
6 Algorithms implemented and tested
3 IP conceived and implemented
Multi-clock periods for a heterogeneous functionning
Development method is satisfying with room for improuvement
Set up the usage of automated development tools
Develop multi-microblazes multi-Ips
Maximise board usages
Completed a full development cycle : objective achieved

## Slide 23
Conclusion
Thank you for you attention